## Slide 1: Anonymity Preserving, Decoupled Distributed Authentication for Multihop IoT Networks
MTP Thesis Defense | Sreeparna Das | Anup Kulkarni | Manas Khatua | IIT Guwahati | June 2026

## Slide 2: Agenda 01 05 04 02 06 03
ProVerif: 19 queries verified under Dolev-Yao model
IoT auth challenges, DAuth baseline, two gaps
4-phase protocol: pseudonym rotation + dual-state desync recovery
LAAKA, Zhou & DAuth: strengths vs limitations
COOJA simulation (100-mote) + RPi 4B hardware benchmarks
Research gaps driving the proposed scheme
Introduction
Proposed Protocol
Security Analysis
Literature Review
Performance & Conclusions
Motivation

## Slide 3: Abstract
The Internet of Things demands lightweight, secure authentication for resource-constrained multihop networks while protecting device privacy. DAuth solves skewed load via decoupled auth-server assignment, but leaves two critical gaps: device identity exposed on open channel enabling cross-session tracking, and single packet loss causes desynchronisation forcing full re-enrolment. We propose pseudonym rotation PID = H(ID_D || m_curr) and dual-state synchronisation. Formally verified via ProVerif (19 queries) and evaluated on COOJA simulation (100-node) and RPi 4B hardware — achieving the lowest overhead among all compared schemes, with full anonymity and desync resilience.
Paper Overview
Contribution 1: Anonymity
Per-session rotating pseudonym PID = H(ID_D || m_curr) replaces real device ID on all open-channel messages. Successive sessions are unlinkable; real ID never leaves the secure enrolment channel.
Contribution 2: Desync Recovery
Dual state (m_curr, m_old, PID_curr, PID_old) at AS and GW silently absorbs one missed key-update packet per epoch — zero re-enrolment penalty on battery-constrained nodes.
1
2

## Slide 4: Why IoT Authentication Is a Hard Problem
30B+ devices by 2030 spanning hospitals, factories, smart cities and homes. Each must prove identity before any data exchange.
Battery-powered, <256 KB RAM, no keyboard. Traditional PKI, TLS and password-based protocols are computationally infeasible.
Every packet is visible to any node in radio range. Replay, impersonation and eavesdropping require zero physical access.
Data traverses 5-20 intermediate hops before reaching the gateway. Trust must be established hop-by-hop without a central authority.
Massive Scale
Severe Resource Constraints
Open Wireless Channel
Multihop Complexity

## Slide 5: The Authentication Architecture Problem
Auth node = parent in RPL routing tree
Popular parents carry disproportionate auth load
Low-degree parents stay idle — capacity wasted
Skewed load grows with tree imbalance
Examples: LightSAE, Li et al., Zheng et al.
Result: load proportional to tree topology;
capable neighbours under-utilised
All auth traffic routes through single gateway
Gateway is a bottleneck in dense multihop networks
Gateway failure stops authentication network-wide
Examples: RAAF-MEC, He et al., Roy et al.
Result: single point of failure; does not
scale to large multihop IoT deployments
Centralized Schemes
Parent-Centric Distributed

## Slide 6: DAuth — The Decoupled Baseline [Das & Khatua, COMSNETS 2026]
1
2
3
Gateway pre-assigns ANY capable node as authentication server — not just the parent. Load distributes evenly across the network. Solves both centralized bottleneck and parent-centric skew.
Device-unique secret derived from a Physically Unclonable Function — never stored, hence un-cloneable. One-way hash accumulator enables group-membership verification without exposing individual secrets.
Enrolment -> Authentication -> Key Exchange -> Data Comm. All operations are hash and XOR only — no ECC, no AES, no PKI. Proven on 802.15.4/RPL networks at 100-node scale.
Decoupled Auth-Server Assignment
PUF + Hash-Accumulator Security
Four-Phase Lightweight Protocol

## Slide 7: DAuth's Two Critical Security Gaps
1
2
3
DAuth transmits real device ID (ID_D) in plaintext on every authentication session. Any adversary in radio range silently captures ID_D. Successive captures from different locations link the same device across sessions — revealing location patterns and usage behaviour. Privacy is violated even when payload content is encrypted.
DAuth stores one nonce m per device. If the Phase-3 key-delivery packet is lost (common in wireless mesh), D and AS hold different m. Next authentication attempt fails immediately — forcing a costly full re-enrolment that drains battery on constrained nodes.
At IoT scale (millions of sessions daily), identity tracking is a persistent, not edge-case threat. Sporadic packet loss in 802.15.4 wireless mesh makes desync a routine occurrence. DAuth needs both fixes to be viable for privacy-sensitive deployments.
Gap 1 — Identity Exposure on Open Channel
Gap 2 — Single-State Desynchronisation
Why Both Gaps Must Be Fixed

## Slide 8: Literature Review: Authentication Scheme Categories
RAAF-MEC, He et al., Roy et al.: Gateway or edge server authenticates all IoT devices. Simple design but single point of failure. Bottleneck grows with network density. Cannot scale to multihop IoT.
LightSAE, Li et al., Zheng et al.: Auth node = parent in routing tree. Better than centralized but creates skewed load. Busy parents starved; idle siblings under-utilized. None provide device anonymity.
LAAKA and Zhou et al.: Provide anonymity via pseudonyms. However, both use centralized auth, lack decoupled design, lack desync recovery, and carry substantially higher computational overhead than hash-only schemes.
Category 1 — Centralized
Category 2 — Distributed / Parent-Centric
Category 3 — Anonymous & Privacy-Preserving

## Slide 9: LAAKA — Ali & Ahmed, Computers & Security 140, 2024
Lightweight Anonymous Authentication and Key Agreement for fog-driven IoT systems. Targets devices communicating via fog computing layer. Provides anonymity and forward secrecy using symmetric cryptography (HMAC, XOR) — no certificate management, no asymmetric operations. Well suited for smart-home and healthcare IoT.
Overview
What LAAKA Does Well
+ Device anonymity via per-session pseudonym
+ Key agreement in a single round-trip
+ Formally verified security properties
+ No asymmetric crypto (low computation)
Critical Limitations vs This Work
- Centralized: all auth via gateway/fog server
- No PUF: key stored in memory (cloneable)
- No desync recovery on packet loss
- ~75% higher energy per round than our scheme
- Not designed for multihop mesh topologies
1
2

## Slide 10: Zhou et al. — IEEE IoT Journal Vol. 11, No. 6, 2024
Security-Enhanced Lightweight Anonymous Authentication for IoT-Based Healthcare. Uses Physically Unclonable Function for device-unique secrets — no long-term key storage. Targets wearable monitors, hospital equipment, implantable sensors. Provides anonymity and session key agreement with formal security proofs.
Overview
What Zhou Gets Right
+ PUF-based: device secret not stored (anti-clone)
+ Anonymity via temporary IDs
+ Healthcare-grade security properties
+ Formal security verification included
Critical Limitations vs This Work
- Centralized architecture: no decoupled auth
- No hash accumulator for group membership
- No desync recovery on packet loss
- ~48% higher energy per round than our scheme
- Not designed for multihop RPL/802.15.4 networks
1
2

## Slide 11: DAuth — Das & Khatua, COMSNETS 2026 (Our Baseline)
First scheme to decouple auth-server assignment from network routing. PUF + hash-accumulator. Lowest computational overhead among all compared schemes. Specifically designed for 802.15.4/RPL multihop networks. Verified on 100-node COOJA simulation and RPi 4B hardware. This work directly extends DAuth with two features.
Overview
Key Innovations in DAuth
+ First decoupled: GW assigns ANY capable node as AS
+ PUF: no long-term secret storage (anti-clone)
+ Hash accumulator: group membership w/o secret exposure
+ All operations hash & XOR only
+ Lowest overhead of any existing comparable scheme
Residual Gaps (Closed by This Work)
- Real ID_D on open channel every session
-> enables cross-session location tracking
- Single-state nonce: packet loss = re-enrol
-> costly on battery-constrained nodes
=> We add pseudonym + dual-state at ~8% extra cost
1
2

## Slide 12: Feature Comparison of Authentication Schemes
Scheme | Dec. | PUF | Acc. | Anon. | Desync | Comp.OH | Msg.OH
RAAF-MEC | ✗ | ✓ | ✗ | ✗ | ✗ | High | Low
SAKMS | ✓ | ✗ | ✗ | ✗ | ✗ | High | Low
Li et al. | ✓ | ✓ | ✗ | ✗ | ✗ | High | Low
Zheng et al. | ✓ | ✓ | ✗ | ✗ | ✗ | Medium | Low
LAAKA | ✗ | ✗ | ✗ | ✓ | ✗ | Low | Low
Zhou et al. | ✗ | ✓ | ✗ | ✓ | ✗ | Medium | Medium
DAuth | ✓ | ✓ | ✓ | ✗ | ✗ | Low | Low
Proposed | ✓ | ✓ | ✓ | ✓ | ✓ | Low | Low
Dec.=Decoupled | Acc.=Hash accumulator | Anon.=Pseudonym anonymity | Desync=Packet-loss recovery without re-enrolment | Comp.OH: Low=Hash/XOR, Med=>2 AES, High=ECC | Msg.OH: Low=1-3 rds, Med=4-5

## Slide 13: Gap 1 — Real Device Identity Exposed on Every Auth Session
Device (D)
Auth Server (AS)
Gateway (GW)
ID_D (plaintext!)
ATTACKER (radio range)
captures ID_D from EVERY session
Same ID_D across sessions -> sessions linked -> device location tracked over time
Why This Is Serious
All three prior schemes (DAuth, LAAKA, Zhou et al.) send real ID_D on the open channel.
Adversary captures it silently, without jamming or any active network disruption.
Over time: same ID + different locations = persistent device location map.
Violates privacy mandates in healthcare, industrial IoT, and smart infrastructure.
Our Fix: PID = H(ID_D || m_curr) sent instead of ID_D — pseudonym changes every session, sessions are unlinkable

## Slide 14: Gap 3 — Overhead Penalty of Existing Schemes
Relative energy per auth round (COOJA, 100-mote network; lower is better)
LAAKA
1.75x
~1.75x more energy (42.8% excess vs our scheme)
Zhou et al.
1.48x
~1.48x more energy (32.4% excess vs our scheme)
Proposed (ours)
1.00x
1.0x Lowest overhead WITH full anonymity + desync recovery
DAuth (base)
0.93x
~0.93x Lightest overall, but NO anonymity, NO desync recovery
0
1.0x
1.75x
(Proposed baseline)
Our scheme adds only ~8% overhead vs DAuth for FULL anonymity + desync recovery — while LAAKA and Zhou use 48-75% more energy per auth round

## Slide 15: Proposed Protocol 04
Two lightweight extensions that close both identified gaps